## Slide 1: 高级计算机体系结构
陈文智
浙江大学计算机学院
chenwz@zju.edu.cn

## Slide 2: 课程网站说明
课程网站：
https://c.zju.edu.cn
使用浙大通行证登录
  如果还没有浙大通行证，需要先激活通行证：
  https://zuinfo.zju.edu.cn
请各位同学在下周上课之前登录一次平台，以便之后将大家添加至班级

## Slide 3: 内容提要及各节间的关系(1)
3.1 流水线技术基础
3.2 How Is Pipelining Implemented?
3.3 The Major Hurdle of Pipelining—Pipeline Hazards
3.4 Extending the MIPS Pipeline to Handle Multicycle Operations
(本科回顾 Appendix A)
流水线技术就是指令重叠执行技术，达到加快运算速度的目的
由于存在三种流水线竞争：结构竞争、数据竞争、控制竞争，导致流水线性能降低，不能运作在理想的重叠状态，需要插入停顿周期，从而使流水线性能降低。

## Slide 4: 内容提要及各节间的关系(2)
3.5 Instruction-Level Parallelism: Concepts and Challenges
(CPI=1)
指令之间可重叠执行性称为指令级并行性（Instruction Parallelism-ILP)。因此进一步研究和开发指令之间的并行性，等于拓宽指令重叠执行的可能性，从而能进一步提高流水线的性能。

## Slide 5: 内容提要及各节间的关系(３)
3.6 Overcoming Data Hazards with Dynamic Scheduling (2.4)
针对流水线数据竞争的动态调度
3.7 Reducing Branch Costs with Dynamic Hardware Prediction (2.3)
针对流水线控制竞争的预测技术

## Slide 6: 内容提要及各节间的关系(4)
3.8 Hardware-Based Speculation (2.6)
进一步开发指令级并行性的动态技术
  跨控制流的动态调度:数据竞争+控制竞争
3.9 Taking Advantage of More ILP with Multiple Issue(2.7)
进一步开发指令级并行性(CPI<1)
  采用单位时钟发射多条指令

## Slide 7: 3.1流水线技术基础
本科回顾------- Appendix A.1
3.1.1 What is pipelining?
3.1.2 Why pipelining ?
3.1.3 Ideal Performance for Pipelining

## Slide 8: 3.1.1 What is pipelining?
Pipelining:
  “A technique designed into some computers to increase speed by starting the execution of one instruction before completing the previous one.”
  ----Modern English-Chinese Dictionary
  implementation technique whereby different instructions are overlapped in execution at the same time.
  implementation technique to make fast CPUs

## Slide 9: Trucking gas from depot to gas station
The steps:
  Get the barrels
  Load them into the truck
  Drive to the gas station
  Unload the gas
  Return for more oil
Let’s do the math
  Each truck can carry 5 barrels
  Can load a truck with 5 barrels in 1 hour
  It takes each truck 1 day to drive to and from gas station
  How many barrels per week are delivered?

## Slide 10: Like a Multi-cycle Processor
What are similar in the steps ?
  Fetch an instruction (Get the barrels)
  Decode the instruction (Load them into the truck)
  ALU OP (Drive to the gas station)
  Memory Access (Unload the gas)
  Write-back (Return for more oil)

## Slide 11: A better way, but dangerous
Roll the barrels down the road
  Big fire hazard

## Slide 12: Big idea: Build a pipeline
Now let’s do the math
  Pipeline can accept 1 barrel every hour
  How many barrels get delivered to the gas station per day?

## Slide 13: Trucking vs. Pipelines
Trucks
  Truck with 5 barrels takes 1 day to drive to and from gas station, while need 2 hours for loading and unloading
  LOTS of TIME when loading area,gas station, and pieces of the road are unused
Pipelines
  Pipeline can accept 1 barrel every hour
  Resources (loading area, gas station,pipelines) are always in use

## Slide 17: What is Pipelining
A pipeline is like an auto assemble line
A pipeline has many stages
Each stage carries out a different part of instruction or operation
The stages, which cooperates at a synchronized clock, are connected to form a pipe
An instruction or operation enters through one end and progresses through the stages and exit through the other end
Pipelining is an implementation technique that exploits parallelism among the instructions in a sequential instruction stream

## Slide 18: 3.1.2 Why pipelining : save time and high utilization factor
Latches, called pipeline registers’ break up computation into 5 stages
Deal 5 tasks at the same time.
Only deal one task each time.
This task takes
“ such a long time”

## Slide 19: Why pipelining: How faster
Can “launch” a new computation every 100ns in this structure
Can finish 107 computations per second
Can launch a new computation every 20ns in pipelined structure
Can finish 5×107 computations per second

## Slide 20: Conclusion
The key implementation technique used to Make fast CPU: decrease CPUtime.
Improving of Throughput ( rather than individual execution time)
Improving of efficiency for resources (functional unit)

## Slide 21: 3.1.3 Ideal Performance for Pipelining
Speedup
Assume: stages: k tasks: n
      Tk＝(k+(n-1))τp
    T1＝ n kτup
τ
T
T
k
1
τ
1) p
(n
τ
k p
nk up
-
+
=
=
peedup
S
＝
Time tasks on unpipelined machine
Time same tasks on pipelined machine
n—→∞ Speedup—→K

## Slide 22: Ideal Performance for Pipelining
If the stages are perfectly balanced, The time per instruction on the pipelined processor equal to:
Time per instruction on unpipelined machine
Number of pipe stages
So, Ideal speedup equal to
Number of pipe stages.

## Slide 23: Why not just make a 50-stage pipeline ?
Some computations just won’t divide into any finer (shorter in time) logical implementation.
5 stages OK
50 stages NO. Sorry!

## Slide 24: Why not just make a 50-stage pipeline ?
Those latches are NOT free, they take up area, and there is a real delay to go THRU the latch itself.
  Machine cycle > latch latency + clock skew
In modern, deep pipeline (10-20 stages), this is a real effect
Typically see logic “depths” in one pipe stage of 10-20 “gates”.
At these speeds, and with this few levels of logic, latch delay is important

## Slide 25: How Many Pipeline Stages?
E.g., Intel
  Pentium III, Pentium 4: 20+ stages
  More than 20 instructions in flight
  High clock frequency (>1GHz)
  High IPC
Too many stages:
  Lots of complications
  Should take care of possible dependencies among in-flight instructions
  Control logic is huge

## Slide 26: 3.2 How Is Pipelining Implemented?
本科回顾------- Appendix A.3
3.2.1 How does instruction Work in the MIPS 5 stage pipeline?
3.2.2 5-stage Version of MIPS Datapath
3.2.3 The MIPS pipelining and some Problems

## Slide 27: Basic of RISC Instruction Set

## Slide 28: MIPS Instruction Format

## Slide 29: MIPS Instruction Format

## Slide 30: Addressing in Jumps and Branches

## Slide 31: 3.2.1 MIPS 5 stage pipeline (1)
The first two stages of MIPS pipeline
IF (Instruction fetch cycle)
  IRMem[PC];
  NPC PC=PC+4;
ID (Instruction decode/register fetch cycle)
  A Regs[rs];
  B Regs[rt];
  Imm sign-extended immediate field of IR;
Note: The first two stages of MIPS pipeline do the same functions for all kinds of instructions.

## Slide 32: MIPS 5 stage pipeline (2)
EX (Execution/effective address cycle)
  Memory reference:
    ALUoutput A+Imm
  Register-Register ALU instruction:
    ALUoutput A func B;
  Register-Immediate ALU instruction:
    ALUoutput A op Imm;
  Branch:
    ALUoutput NPC+(Imm <<2 );
    Cond (A==0)

## Slide 33: MIPS 5 stage pipeline (2)
MEM(Memory acces/branch completion cycle)
  Memory reference:
    LMD Mem[ALUoutput] or
    Mem[ALUoutput] B
  Branch:
    If (cond) PC ALUoutput
WB (Write back cycle)
  Register-Register ALU instruction
    Regs[rd]  ALUoutput;
  Register-Immediate ALU instruction
    Regs[rt] ALUoutput;
  Load Instruction:
    Regs[rt] LMD;

## Slide 35: 3.2.3 The MIPS pipelining

## Slide 36: Table: Events on every stage
Stage | Any instruction |  | 
IF | IF/ID.IRMem[PC]; IF/ID.NPC, PC (if ((EX/MEM.opcode==branch)&EX/MEM.cond) { EX/MEM.ALUoutput} else {PC+4}); |  | 
ID | ID/EX.A Regs[IF/ID.IR[rs]]; ID/EX.B Regs[IF/ID.IR[rt]]; ID/EX.NPC IF/ID.NPC; ID/EX.IR IF/ID.IR; ID/EX.Imm sign-extend(IF/ID.IR[immediate field]); |  | 
 | ALU instruction | Ld/st instruction | Branch instruction
EX | EX/MEM.IR ID/EX.IR; EX/MEM.ALUoutput ID/EX.A func ID/EX.B; or EX/MEM.ALUoutput ID/EX.A op ID/EX.Imm; | EX/MEM.IR ID/EX.IR; EX/MEM.ALUoutput ID/EX.A + ID/EX.Imm; EX/MEM.B ID/EX.B; | EX/MEM.ALUoutput ID/EX.NPC + (ID/EX.Imm<<2); EX/MEM.cond (ID/EX.A==0);
MEM | MEM/WB.IR  EX/MEM.IR; MEM/WB.ALUoutput EX/MEM.ALUoutput; | MEM/WB.IR  EX/MEM.IR; MEM/WB.LMD Mem[EX/MEM.ALUoutput]; Or MEM/WB.LMD Mem[EX/MEM.ALUoutput]; | 
WB | Regs[MEM/WB.IR[rd]] MEM/WB.ALUoutput; or Regs[MEM/WB.IR[rt]] MEM/WB.ALUoutput; | For Load only; Regs[MEM/WB.IR[rt]] MEM/WB.LMD | 

## Slide 37: Advanced pipeline
store
load
pipeline
registers or
latches
Why need to add this line?

## Slide 38: Problems that pipelining introduces
一、There is conflict about the memory !
Mem
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Ld/St
Instr 1
Instr 2
Instr 3
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Reg
Mem
Reg

## Slide 39: Separate instruction and data memories
use split instruction and data cache
the memory system must deliver 5 times the bandwidth over the unpipelined version.
IM
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Ld/St
Instr 1
Instr 2
Instr 3
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
Reg
DM
Reg

## Slide 40: The conflict about the registers !

## Slide 41: Sometimes we can redesign the resource
Allow WRITE-then-READ in one clock cycle (double pump)
  Two reads and one write required per clock.
  Need to provide two read port and one write port.

## Slide 42: The conflict about the data

## Slide 43: Conflict occurs when PC update

## Slide 44: Must latches be engaged ? Yeah !
Ensure the instructions in different stages do not interfere with one another .
Through the latches, can the stages be combined one by one to form a pipeline.
The latches are the pipeline registers , which are much more than those in multi-cycle version
  IR: IF/ID.IR; ID/EX.IR; EX/DM.IR; DM/WB.IR
  B: ID/EX.B; EX/DM.B
  ALUoutput: EX/DM.ALUoutput, DM/WB.ALUoutput

## Slide 45: 3.3 The Major Hurdle of Pipelining—Pipeline Hazards
本科回顾------- Appendix A.2
3.3.1 Taxonomy of hazard
3.3.2 Performance of pipeline with Hazard
3.3.3 Structural hazard
3.3.4 Data Hazards
3.3.5 Control Hazards

## Slide 46
THANK YOU
THANK YOU